## Slide 1
Argentometry
«General pharmaceutical chemistry »
Associate Professor Gureeva E.S.

## Slide 2
Precipitation titration
Precipitation titration is a group of titrimetric methods of analysis based on the formation of low solubility compounds that are released from solution as precipitate.
Requirements:
The precipitate must be practically insoluble, i.e. the solubility of the precipitate must not exceed 10-5 mol/l;
The precipitation shall be sufficiently rapid;
The titration results should not be distorted by adsorption (co-precipitation) phenomena;
It shall be possible to fix the point of equivalence in the titration.

## Slide 3
Classification of precipitation titration methods
According to the nature of the active reagent interacting with the substances to be determined:
Argentometry (AgN03),
Thiocyanatometry (KNCS or NH4NCS),
Mercurometry (Hg2(NO3)2),
Hexacyanoferratometry (K4[Fe(CN)6])
Sulfatometry (H2S04)
Barimetry (BaC12).
In terms of technique,
direct,
reverse titration.
Precipitation titration

## Slide 4
Argentometry
Argentometric titration is a titrimetric method of analysis based on the formation of low soluble silver compounds.
The argentometric titrimetric method of analysis is based on the use of a standard solution of silver nitrate as precipitant:
Аg+ + Наl- ↔ АgНаl↓
A 0.1 mol/L standard solution of silver nitrate can be prepared:
as a primary standard solution;
secondary standard solution.

## Slide 5
Determining the titration endpoint
Indicator-free methods
Chloride ions are determined by the so-called equal clouding method (Gay-Lussac method). In this method the analysed solution is titrated with a standard solution of silver nitrate, the end of the titration is determined by taking two samples of the titrated solution into two tubes near the titration endpoint:
- in one of them a drop of a standard solution of silver nitrate is added,
- in the other one a drop of a standard solution of sodium chloride of the same concentration.
The under-titrated solution shows clouding in the tube with silver nitrate, the over-titrated solution shows clouding in the tube with sodium chloride. At the final titration point, the solution in both tubes has the same turbidity.
Argentometry

## Slide 6
Indicator-free methods
Bromide and iodide ions are determined by the method of enlightenment. Its essence lies in the fact that when small portions of a standard silver nitrate solution are added to the analyzed solution from the burette, a colloidal silver bromide solution is formed at the beginning, and at the moment of equivalence, colloidal particles coagulate and precipitate in the form of curd flakes, while the solution is clarified.
Of the modern Indicator-free methods in argentometry, potentiometric determination of the equivalence point using silver or halide-selective electrodes is most often used.
Argentometry
Determining the titration endpoint

## Slide 7
Indicator methods
Depending on the indicator used in argentometry , the following methods are distinguished:
Mohr method based on the reaction between silver ions and halide ions in the presence of an indicator - a solution of potassium chromate;
Volhard’s method (thiocyanatometry), based on the reaction between silver ions and thiocyanate ions in the presence of iron (III) ions as an indicator;
Fajans method is based on the use of adsorption indicators.
Argentometry

## Slide 8
Mohr method
Direct titration
Titrant solution of 0.1 (or 0.05; 0.02; 0.01) mol/l silver nitrate
Indicator solution 0.01 mol/l of potassium chromate
Аg+ + Наl- ↔ АgНаl↓
Cl- + Ag+ ↔ AgCl ↓ white
Br- + Ag+ ↔ AgBr ↓ yellowish white
K2CrO4 + 2AgNO3 = Ag2CrO4↓ + 2KNO3
brick-red sediment
Sedimentary indicators are substances released from a solution in the form of a precipitate in a well-marked form at or near the equivalence point.
Argentometry

## Slide 9
Conditions of titration by the Mohr method:
Titration should be carried out in a neutral or slightly alkaline medium (6.5 ≤ pH ≤ 10).
The solution should be free of:
Pb2+, Ba2+, Hg2+ cations and others forming chromate precipitates with indicator anions
PO43-, CO32-, C2O42-, AsO43- anions and others forming precipitates with silver ions.
Near the end point of titration, the solution must be titrated slowly, with vigorous stirring, in order to reduce the error due to adsorption.
It is impossible to titrate colored solutions, as they will mask the Ag2CrO4 coloring, which will make it difficult to fix the end point of titration.
Argentometry
Mohr method

## Slide 10
The Mohr method is applicable for the determination of chlorides and bromides, including pharmaceuticals, which include chloride and bromide ions.
The Mohr method cannot be used to determine:
iodide and rhodanide ions due to their strong adsorption on the sediment surface;
salts of hydrochloric acids and weak bases, since as a result of hydrolysis, an acidic medium is formed in their solutions:
NH4+ + Н2О ↔ NН3 ∙ Н2О + Н+
Argentometry
Mohr method

## Slide 11
Application in pharmaceutical analysis
The Mohr method is mainly used for the quantification of sodium and potassium chlorides and bromides in neutral or weakly alkaline solutions.
The drugs potassium chloride, sodium chloride, potassium bromide and sodium bromide are titrated in a neutral medium, potassium chromate is used as an indicator.
The excess titrant (the first drop) interacts with the indicator to form an orange-red precipitate, according to which the end point of titration is set:
Argentometry
Mohr method

## Slide 12
Volhard’s method
The Volhard’s method is based on titration of a solution containing silver ions with standard solutions of NH4NCS or KNCS:
Ag+ + NCS- ↔ AgNCS↓
The indicator in this method is iron-ammonium alum NH4[Fe(SO4)2] ∙12Н2О.
NH4[Fe(SO4)2] + 3NH4NCS ↔ Fе(NСS)3 + 2(NH4)2SO4
As standard solutions are used:
in the method of direct titration - a solution of ammonium thiocyanate or potassium thiocyanate;
in the reverse titration method – the solutions of silver nitrate and ammonium or potassium thiocyanate.
Argentometry

## Slide 13
Preparation of NH4NCS solution.
Ammonium thiocyanate is not a standard substance, since the salt is hygroscopic. Therefore, a solution of the required concentration is prepared from it - approximately 0.1 or 0.05 mol / l, and then it is standardized according to the standard substance AgNO3 or according to the standard solutionАgNО3.
Conditions of titration by the Volhard’smethod:
Titration should be performed in an acidic environment to prevent hydrolysis of the indicator .
During titration, the solution must be vigorously mixed to reduce the error due to the adsorption of ions on the surface of the precipitate.
The analyzed solution should be free of:
mercury salts (I) and (II) reacting with NCS-ions:
oxidants KBrO3, KMnO4 and other oxidizing NCS-ions;
anions F-, PO43-, C2O42- and others forming strong complexes with the indicator
Argentometry
Volhard’s method

## Slide 14
Determination of Ag+ ions by the Volhard’s method (direct titration)
A standard solution of ammonium thiocyanate reacts primarily with silver ions, forming a unsolvable compound:
Ag+ + NH4NCS ↔ AgNCS + NH4+
At the end point of titration, the excess titrant drop reacts with Fe3+ ions and turns the solution red:
NH4[Fe(SO4)2] + 3NH4NCS ↔ Fе(NСS)3 + 2(NH4)2SO4
Argentometry
Volhard’s method

## Slide 15
Application of the Volhard’s method (direct titration) in pharmaceutical analysis
Determination of silver cations in colloidal solutions (collargol and protargol). At the beginning, colloidal preparations are destroyed by boiling in a mixture of concentrated sulfuric and nitric acids. The resulting silver ions are then titrated with ammonium thiocyanate. Indicator iron-ammonium alum.
Ag+ + NH4NCS ↔ AgNCS + NH4+
NH4[Fe(SO4)2] + 3NH4NCS ↔ Fе(NСS)3 + 2(NH4)2SO4
Collargol should contain at least 70% silver, and protargol — 7.5-8.5%.
Argentometry
Volhard’s method

## Slide 16
Determination of anions by the Volhard’s method (reverse titration)
Reverse titration is used to determine anions. To the analyzed solution, double the minimum, precisely measured volume of the standard silver nitrate solution (1st working solution) is added, which reacts with the determined anions, for example, chloride ions:
AgNO3 + Сl- ↔ AgCl↓ + NO3 -
The unreacted silver nitrate residue is titrated with a second standard solution of ammonium thiocyanate:
AgNO3 + NH4NCS ↔ AgNCS↓ + NH4NO3
at the end of titration, an excess drop of NH4NCS solution reacts with the indicator:
NH4[Fe(SO4)2] + 3NH4NCS ↔ Fе(NСS)3 + 2(NH4)2SO4
and the solution turns red.
Argentometry
Volhard’s method

## Slide 17
Advantages of the Volhard’s method
In comparison with the Mohr method, the Folgard method has a number of advantages:
the determination of Ag+, Cl-, Br-, I-, NCS- is performed in an acidic medium;
the cations Ba2+, Pb2+ and others that interfere with the determination of anions by the Mohr method do not interfere with their determination by Volhard’s.
Argentometry
Volhard’s method

## Slide 18
Application of the Volhard’s method (reverse titration) in pharmaceutical analysis
Bromisoval
Titrant NH4SCN
Indicator NH4[Fe(SO4)2]
Argentometry
Volhard’s method

## Slide 19
Bromcamphora
Titrant NH4SCN
Indicator NH4[Fe(SO4)2]
Argentometry
Volhard’s method
Application of the Volhard’s method (reverse titration) in pharmaceutical analysis

## Slide 20
Mercaptopurine
Titrant NH4SCN
Indicator NH4[Fe(SO4)2]
Argentometry
Volhard’s method
Application of the Volhard’s method (reverse titration) in pharmaceutical analysis

## Slide 21
Fajans method
The Fajans method is based on direct titration of anions (halides, cyanides, thiocyanates) with a standard silver nitrate solution in the presence of adsorption indicators.
Silver halides are prone to the formation of colloidal solutions. In the presence of an excess of Hal ions due to the adsorption of AgHal particles acquire a negative charge:
In the presence of an excess of Ag+ ions, they acquire a positive charge:
Argentometry

## Slide 22
Adsorption indicators are substances whose adsorption or desorption by sediment is accompanied by a change in color at or near the equivalence point.
As adsorption indicators are used:
Bromophenol Blue
Sodium Eosinate
Fluorescein
Argentometry
Fajans method

## Slide 23
Conditions of titration by the Fajans method
Titration should be performed at a certain pH value, as this significantly affects the ionization of the indicator.
Titration with an adsorption indicator should be carried out with a large sediment surface. This is achieved when the precipitate is present in the form of colloidal particles. For this purpose, protective colloids are added to the titrated solution - dextrin, starch, etc.
It is necessary that the indicator ions are adsorbed by the sediment much weaker than the ions being determined, otherwise the indicator ions will be adsorbed much earlier than the moment of equivalence, which will lead to underestimated analysis results.
Fluorescein can be used in the determination of chlorides, bromides, iodides and rhodanides, eosin - only in the titration of bromides, iodides and rhodanides. Titration of chlorides in the presence of eosin does not give accurate results, since in this case the staining of the precipitate occurs before the end of the reaction.
Titration cannot be carried out in direct sunlight, since adsorbed indicators greatly increase the sensitivity of salts to light.
Argentometry
Fajans method

## Slide 24
Application of the Fajans method in pharmaceutical analysis
Potassium iodide
Sodium iodide
Titrant AgNO3
Indicator Sodium Eosinate
Color transition from yellow to pink
Argentometry
Fajans method

## Slide 25
Diphenhydramine
Titrant AgNO3
Indicator Bromophenol Blue
Color transition from greenish-yellow to purple
Argentometry
Fajans method
Application of the Fajans method in pharmaceutical analysis

## Slide 26
Novocaine
Titrant AgNO3
Indicator Bromophenol Blue
Color transition from greenish-yellow to purple
Argentometry
Fajans method
Application of the Fajans method in pharmaceutical analysis

## Slide 27
Thank you for attention!